## Slide 1: INTRODUCTION TO CACHE MEMORY.
PRESENTED BY GROUP 3

## Slide 2: GROUP 3
OLADEJI DANIEL
ODEH ISAAC
ADEWESO ADEDAMOLA

## Slide 3: WHAT IS CACHE MEMORY ?
Cache memory is a chip-based computer component that makes retrieving data from the computer's memory more efficient. It acts as a temporary storage area that the computer's processor can retrieve data from easily. This temporary storage area, known as a cache, is more readily available to the processor than the computer's main memory source, typically some form of DRAM.
Cache memory is sometimes called CPU(central processing unit) memory because it is typically integrated directly into the CPU chip or placed on a separate chip that has a separate bus interconnect with the CPU. Therefore, it is more accessible to the processor, and able to increase efficiency, because it's physically close to the processor.

## Slide 4: WHAT IS CACHE MEMORY ?
In order to be close to the processor, cache memory needs to be much smaller than main memory. Consequently, it has less storage space. It is also more expensive than main memory, as it is a more complex chip that yields higher performance.
What it sacrifices in size and price, it makes up for in speed. Cache memory operates between 10 to 100 times faster than RAM, requiring only a few nanoseconds to respond to a CPU request.

## Slide 5: TYPES OF CACHE MEMORY
Cache memory is fast and expensive. Traditionally, it is categorized as "levels" that describe its closeness and accessibility to the microprocessor. There are three general cache levels:
L1 or Level 1 Cache: It is the first level of cache memory that is present inside the processor. It is present in a small amount inside every core of the processor separately. The size of this memory ranges from 2KB to 64 KB.
L2 or Level 2 Cache: It is the second level of cache memory that may present inside or outside the CPU. If not present inside the core, It can be shared between two cores depending upon the architecture and is connected to a processor with the high-speed bus. The size of memory ranges from 256 KB to 512 KB.
L3 or Level 3 Cache: It is the third level of cache memory that is present outside the CPU and is shared by all the cores of the CPU. Some high processors may have this cache. This cache is used to increase the performance of the L2 and L1 cache. The size of this memory ranges from 1 MB to 8MB.

## Slide 6: CACHE MEMORY MAPPING
Caching configurations continue to evolve, but cache memory traditionally works under three different configurations:
Direct Mapped Cache: In this setup, each data block is assigned to a specific location in the cache. Visualize it as a table with three columns: one for the actual data, one for an address tag, and one for a flag indicating the presence of valid data.
Fully Associative Cache Mapping: Similar in structure to direct mapping but with greater flexibility. It allows memory blocks to be placed in any available cache location, unlike direct mapping, which assigns them to specific locations.
Set Associative Cache Mapping: A middle ground between direct and fully associative mapping. Here, memory blocks are divided into subsets, and each block can be cached in any location within its subset. This is sometimes referred to as "N-way set associative mapping," where "N" represents the number of possible cache locations in the L1 cache.

## Slide 7: DATA WRITING POLICIES
Data can be written to memory using a variety of techniques, but the two main ones involving cache memory are:
Write-through. Data is written to both the cache and main memory at the same time.
Write-back. Data is only written to the cache initially. Data may then be written to main memory, but this does not need to happen and does not inhibit the interaction from taking place.

## Slide 8: ROLES OF CACHE MEMORY.
Cache memory plays a crucial role in computer systems.
It provide faster access.
It acts buffer between CPU and main memory(RAM).
Primary role of it is to reduce average time taken to access data, thereby improving overall system performance.

## Slide 9: BENEFITS OF CACHE MEMORY
Faster access: Faster than main memory. It resides closer to CPU , typically on same chip or in close proximity. Cache stores subset of data and instruction.
Reducing memory latency: Memory access latency refers to time taken for processes to retrieve data from memory. Caches are designed to exploit principle of locality.
Increasing effective CPU utilization: Cache memory allows CPU to operate at a higher effective speed. CPU can spend more time executing instruction rather than waiting for memory access. This leads to better utilization of CPU’s processing capabilities and higher overall system performance.
Enhancing system scalability: Cache memory helps improve system scalability by reducing impact of memory latency on overall system performance.

## Slide 10: CACHE VS. RAM
CACHE | RAM
It is ensured that data in RAM are loaded before access to the CPU. This eliminates RAM miss never. | RAM is larger in size compared to cache. Memory ranges from 1MB to 16GB
It holds frequently accessed data. | It stores data that is currently processed by the processor.
OS interacts with primary memory to get data to be stored in Cache. | OS interacts with secondary memory to get data to be stored in Primary Memory or RAM
CPU searches for data in Cache, if not found cache miss occur. | It is ensured that data in RAM are loaded before access to the CPU. This eliminates RAM miss never.

## Slide 11: CACHE MEMORY CALCUALTIONS
Cache memory is primarily associated with two key calculations:
Cache Hit Ratio: This calculation measures the efficiency of the cache system. It's the ratio of cache hits (data found in the cache) to total memory access requests. A high cache hit ratio indicates that the cache is effectively reducing the need to access slower main memory.
Cache Hit Ratio (%) = (Cache Hits / Total Memory Accesses) * 100
Cache Size and Mapping: The size of the cache and the way it's mapped can affect its performance. The calculation for cache size often involves factors like cache associativity (how data is mapped to cache sets) and the block size (size of data stored in each cache line). These parameters impact the effectiveness of the cache.
Different cache organizations, such as direct-mapped, set-associative, or fully associative, will have different calculations for determining cache size and mapping efficiency.
These calculations are crucial for optimizing cache memory to improve overall system performance.

## Slide 12: CACHE MEMORY CALCULATIONS
Example 1:
Suppose a computer system has a cache memory with 80 cache hits out of a total of 100 memory access requests.
Cache Hit Ratio = (80 / 100) * 100 = 80%
This means that 80% of the time, the required data was found in the cache, resulting in a relatively high cache hit ratio.
Example 2:
In another scenario, the cache experiences 150 hits out of 200 memory accesses.
Cache Hit Ratio = (150 / 200) * 100 = 75%
Here, the cache hit ratio is 75%, indicating that the cache was effective in reducing the number of accesses to slower main memory.

## Slide 13: CACHE MEMORY CALCULATIONS
Example 1:
Consider a direct-mapped cache with a total size of 64 KB (kilobytes) and a block size of 4 KB. In this case, the number of cache lines (blocks) can be calculated as follows:
Number of Cache Lines = Cache Size / Block Size = 64 KB / 4 KB = 16
This means there are 16 cache lines in the direct-mapped cache.
Example 2:
Now, let's look at a set-associative cache with a total size of 128 KB and a set-associativity of 2 (each set contains 2 lines). The number of sets can be calculated as follows:
Number of Sets = Cache Size / (Set Associativity * Block Size) = 128 KB / (2 * 4 KB) = 16
In this example, there are 16 sets in the set-associative cache.
These examples illustrate how to calculate cache hit ratio and aspects of cache size and mapping for different cache architectures.

## Slide 14
THANK YOU !!!